## Slide 1: Performance Optimization for Isolated Driver Domains.
Sushrut Shirole

## Slide 2: Typical OS components
Operating System
Hardware
User
Process
User
Process
User
Process

## Slide 3: Device Driver
Operating System
Hardware
User
Process
User
Process
User
Process
Network
SATA
A device driver is a computer program which acts as a translator between the hardware device and the application or the operating system.

## Slide 4: Why Device Driver isolation ?
An analysis of the Linux kernel code using Coverity
    1000 bugs in the Linux kernel 2.4.1
    950 bugs in the Linux kernel 2.6.9
    53% of the bugs are present in the device driver portion of the kernel
    Any portion of the kernel can overwrite data structure in the kernel space
    This causes a bug in a device driver to corrupt the memory of other kernel components

## Slide 5: Why Device Driver isolation ?
  Underlying cause of unreliability in operating systems is the lack of isolation between device drivers and a Linux kernel

## Slide 6: Xen’s Isolated Driver Domain
The Xen hypervisor isolates the device driver by running it in a separate domain called Driver Domain
Application
TCP/IP stack
Split Device Driver
Front end
Xen
Shared Memory Segment
Split Device Driver
Back end
Real Device driver
Physical Device
Hardware
Domain 0
Domain U Guest

## Slide 7: Xen Split Device Driver
Isolated Driver Domain code is not available.
The Isolated Driver Domain follows split device driver.

## Slide 8: Isolated Device Driver (IDDR)
Re-implementation of the Isolated Driver Domain
Also follows the Xen split device driver model
We refer the re-implementation of Isolated Driver Domain as base IDDR system
One with the performance improvement is referred as the new IDDR system

## Slide 9: Properties of the Base IDDR
Strong isolation: A bug within a device driver does not affect the other kernel component.
Transparency: User need not be aware of the system architecture to run the application.
Compatibility: Existing drivers and applications are compatible with the new architecture. Changes to the device driver and applications are not required to run the system.

## Slide 10: Components of the IDDR system
Application domain
User process
SATA
File system
Driver domain

## Slide 11: Components of the IDDR system
Application domain
User process
SATA
File system
Driver domain
Read Write Request
/dev/sdd
How to forward to the Driver domain?
Frontend
Communication Channel
How to receive request from the application domain ?
Backend

## Slide 12: Components of the IDDR system
Frontend Driver
  Provides an interface for applications
Backend Driver
  Accepts the requests and sends back responses
Communication Module

## Slide 13: Communication module
Application domain
User process
SATA
File system
Frontend
Backend
Driver domain
Share read write data
Communication component
Event notification
Send/receive request/response

## Slide 14: Implementation of the IDDR system
Ring buffer
Event channel
Shared
pages
Communication module
Application domain
User process
SATA
File system
Frontend
Backend
Driver domain

## Slide 15: Implementation of the IDDR system
File system
Frontend
User process
Ring buffer
Event channel
Shared
pages
Communication module
Application domain
SATA
Backend
Driver domain
Device queue

## Slide 16: Design Goals of the New IDDR System
Performance improvement: The design goal of the New IDDR system is to improve the performance of the base IDDR system without compromising any properties of it.
The reason for the performance deterioration of the IDDR system is :
The hypervisor layer.
Extra data copy between the domains.
Overhead due to the communication between the domains.

## Slide 17: The hypervisor layer
Hypervisor runs at most privileged level
Guest os runs at less privileged level
Operations such as page table updates (memory management) takes more time in guest operating system due to hypervisor layer.
User app
Guest OS
Xen
Host computer system hardware
Ring 3
Ring 2
Ring 1
Ring 0
Hypercall
dom0
Privileged
instruction
/syscall
Ring 0
Ring 3
Ring 2
Ring 1

## Slide 18: Data Copy Overhead
In a usual system :
Data is copied from
User space -> kernel space
Kernel space -> Socket buffer (physical nework)
Application
TCP/IP stack
Device Driver
Physical Device
Hardware
Domain U Guest

## Slide 19: Data Copy Overhead
In split device driver
Guest user space -> Guest kernel space
Guest kernel space -> shared memory
Shared memory -> physical device
Application
TCP/IP stack
Split Device Driver
Front end
Xen
Shared Memory Segment
Split Device Driver
Back end
Real Device driver
Physical Device
Hardware
Domain 0
Domain U Guest

## Slide 20: Communication Overhead
Communication between the domains to share requests and responses
Requests and responses are notified by software interrupt
Software interrupt causes rescheduling of the domain – Context switch
Context switch deteriorates the performance

## Slide 21: Cost of Context Switch
Direct cost : Cost required to
  save and restore processor registers
  execute scheduler code
  reload the TLB entries
  flush pipeline
Indirect cost
  Processor pollution: cached entries are removed/ updated from i, d, L2, L3 cache, TLB, etc.
  Cache interference

## Slide 22: Solution
Spinning
  Read request thread - Frontend
    Thread runs in the backend driver
    Spins for some time waiting for requests
  Read response thread - Backend
    Thread runs in the frontend driver
    Spins for some time waiting for responses

## Slide 23: New IDDR system
Application domain
User process
Driver domain
SATA
File system
Frontend
Backend
Ring buffer
Event channel
Read request
Is backend thread running ?
Status :
SLEEPING
Status :
SLEEPING
Buffer
NO. Wake up.
Status :
RUNNING
Spin for some time and check for requests in buffer. Is request available ? NO
Yes. PUT REQUEST in the Ring buffer.
Yes: Copy/get request.
Is frontend thread running ?
NO. Wakeup.
Status :
RUNNING
Spin some time. If response is available then return it to user process. Is response available ? NO
Buffer
Yes. Response is available. Copy data to user buffer.
Shared
pages
Read response
thread
Read request
thread

## Slide 24: Split device driver vs base IDDR system
Loop device random reads
Ramdisk random writes

## Slide 25: Base IDDR vs New IDDR
Random read writes - Ramdisk
Random reads - Ramdisk

## Slide 26: Base IDDR vs New IDDR
Random writes - Ramdisk
Random reads - Loop device

## Slide 27: Base IDDR vs New IDDR
Random writes – Loop device
Random reads+writes loop device

## Slide 28: Trade-off

## Slide 29: Conclusion

## Slide 30: Questions ?

## Slide 31
Application
TCP/IP stack
Split Device Driver
Front end
Xen
Shared Memory Segment
Split Device Driver
Back end
Real Device driver
Physical Device
Hardware
Domain 0
Domain U Guest

## Slide 32
Application
TCP/IP stack
Split Device Driver
Front end
Xen
Shared Memory Segment
Split Device Driver
Back end
Real Device driver
Physical Device
Hardware
Domain 0
Domain U Guest

## Slide 33
Domain 0 guest
Domain U Guest
xen
Hardware
Split Device drivers
Split Device drivers
Applications
Device Drivers
Domain U guest
Split Device drivers
Xen controlled user interface
NFS client
Applications
NFS client
Virtual CPU
Virtual memory
Scheduling
Physical CPU
Physical memory
Network